## Slide 1: Data Link layer and Physical Layer
Dr. Geetha. V
Dept of IT,
NITK Surathkal

## Slide 2: Index
Ethernet (IEEE 802.3)
Functions of Data Link Layer
  Error Control
  Flow Control
  Medium Access Control
Token Ring (IEEE 802.5),
Wireless (IEEE 802.11),
WPAN (IEEE 802.15.4)

## Slide 3: Ethernet (IEEE 802.3)
Ethernet: It is a LAN protocol that is used in Bus and Star topologies and implements CSMA/CD as the medium access method
Original (traditional) Ethernet developed in 1980 by three companies: Digital, Intel, Xerox (DIX).
In 1985, the Computer Society of the IEEE started a project, called Project 802, to set standards to enable intercommunication among equipment from a variety of manufacturers.
  Current version is called IEEE Ethernet

## Slide 4: Ethernet (IEEE 802.3)
Bus Topology
Broadcast in nature
Uses Medium Access Control to share the medium

## Slide 5: Ethernet
In IEEE 802.3 Ethernet Data link layer is split into two sublayers:
  Bottom part: MAC
    The frame is called IEEE 802.3
    Handles framing, MAC addressing, Medium Access control
    Specific implementation for each LAN protocol
      Defines CSMA/CD as the access method for Ethernet LANs and Token passing method for Token Ring.
    Implemented in hardware
  Top part: LLC (Logical Link Control)
    The subframe is called IEEE 802.2
    Provides error and flow control if needed
    It makes the MAC sublayer transparent
      Allows interconnectivity between different LANs data link layers
    Used to multiplex multiple network layer protocols in the data link layer frame
    Implemented in software

## Slide 6: Ethernet
Frame formats. (a) DIX Ethernet , (b) IEEE 802.3
  Preamble:The preamble consists of a 56-bit (seven-byte) pattern of alternating 1 and 0 bits
  Dest and Source address
  Type: 0x0800 – IPv4, 0x0806-ARP, 0x86DD –IPv6
  SoF: Start of Frame, 10101011
  Length: range is 0 to 65534, but limitation 1500
FCS
FCS

## Slide 7: Ethernet Address
Six bytes = 48 bits
Flat address not hierarchical
Burned into the NIC ROM
First three bytes from left specify the vendor. Cisco 00-00-0C, 3Com 02-60-8C and the last 24 bit should be created uniquely by the company
Destination Address can be:
  Unicast: second digit from left is even (one recipient)
  Multicast: Second digit from left is odd (group of stations to receive the frame – conferencing applications)
  Broadcast (ALL ones) (all stations receive the frame)
Source address is always Unicast

## Slide 9: Unicast /Multicast Address

## Slide 10: Transmission Medium

## Slide 11
Categories of traditional Ethernet
<data rate><Signaling method><Max segment length or cable type>

## Slide 12: IEEE 802.3 Cable Types
Name | Cable Max. | Max Cable Segment Length | Nodes /segment
10Base5 | thick coax | 500 meters | 100
10Base2 | thin coax | 185 meters | 30
10BaseT | twisted pair | 100 meters | 1
10BaseF | Fiber Optic | 2Km | 1
Toplogy
Bus
Bus
Star
Star

## Slide 13
10Base5 implementation

## Slide 14: Fast Ethernet
100 Mbps transmission rate
same frame format, media access, and collision detection rules as 10 Mbps Ethernet
can combine 10 Mbps Ethernet and Fast Ethernet on same network using a switch
media: twisted pair (CAT 5) or fiber optic cable (no coax)
Star-wire topology
  Similar to 10BASE-T
CAT 3
CAT 5

## Slide 15: Gigabit Ethernet
Speed 1Gpbs
Minimum frame length is 512 bytes
Operates in full/half duplex modes mostly full duplex

## Slide 16
Figure 13.22 Topologies of Gigabit Ethernet

## Slide 18: Index
Ethernet (IEEE 802.3)
Functions of Data Link Layer
  Error Control
  Flow Control
  Medium Access Control
Token Ring (IEEE 802.5),
Wireless (IEEE 802.11),
WPAN (IEEE 802.15.4)

## Slide 19: Ethernet
Frame formats. (a) DIX Ethernet , (b) IEEE 802.3
  Preamble:The preamble consists of a 56-bit (seven-byte) pattern of alternating 1 and 0 bits
  Dest and Source address
  Type: 0x0800 – IPv4, 0x0806-ARP, 0x86DD –IPv6
  SoF: Start of Frame, 10101011
  Length: range is 0 to 65534, but limitation 1500
FCS
FCS

## Slide 20: Error Control Techniques
One dimensional Parity
Two Dimensional Parity
Checksum
Cyclic Redundancy Code
Hamming Code

## Slide 21: 1. Parity Check
Even Parity: number of 1’s is even
Odd Parity: number of 1’s is even
Cannot identify even number of changes

## Slide 22: 1. Parity Check
Even Parity: number of 1’s is even
Odd Parity: number of 1’s is even
Cannot identify even number of changes

## Slide 23: 2. 2D Parity Check
2D parity Check
D7 | D6 | D5 | D4 | D3 | D2 | D1 | Even Parity
1 | 0 | 1 | 0 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 0 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0 | 1 | 1 | 1
0 | 0 | 1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 1 | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 1 | 0 | 0 | 0 | 1

## Slide 24: 2. 2D Parity Check
2D parity Check : Error Checking: Parity not matching
D7 | D6 | D5 | D4 | D3 | D2 | D1 | Even Parity
1 | 0 | 1 | 0 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 0 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0 | 1 | 1 | 1
0 | 0 | 1 | 0 | 1 | 1 | 0 | 0 (1)
1 | 1 | 0 | 1 | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 1 | 0 (1) | 0 | 0 | 1

## Slide 25: 2. 2D Parity Check

## Slide 26: 3. Checksum

## Slide 27: 4. Cyclic Redundancy Code
Representation of bits in polynomial form

## Slide 28: 4. Cyclic Redundancy Code

## Slide 29: 4. Cyclic Redundancy Code
Generator polynomial: x3+1 (1001)
R= highest power of X
Data Bits: 11010011
Now Dividend is 11010011000
Its polynomial
D=11010011 | R=000
x10+x9+x7+x4+x3

## Slide 30: 4. Cyclic Redundancy Code
Sender side
Divide the data (D * 2r XOR R) with generated polynomial.
Compute with modulo 2 arithmetic => XOR at each stage
Add the Remainder to Data and send it to receiver.

## Slide 31: 4. Cyclic Redundancy Code
Receiver side:
Received data
Generated polynomial
If remainder is zero, no error in received data
If non zero remainder it indicates error. Then discard the frame and ask for retransmission

## Slide 32: 4. Cyclic Redundancy Code
Following types of errors can be detected by a G(x) with the stated properties
  All single-bit errors, as long as the xk and x0 terms have nonzero coefficients
  All double-bit errors, as long as G(x) has a factor with at least three terms
  Any odd number of errors, as long as G(x) contains the factor (x+1)
  Any “burst” error for which the length of the burst is less than k bits.

## Slide 33: 4. Cyclic Redundancy Code
International Standard Generator Polynomial

## Slide 35: 5. Hamming Code
Finding number of redundant bits
2r >=m+r+1
where m= number of Data bits and
r = number of redundant bits
If m=7 bits then r=?
24 ≥ 7 + 4 + 1 so r= 4 bits

## Slide 37: 5. Hamming Code
 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
 | D6 | D5 | D4 | R8 | D3 | D2 | D1 | R4 | D0 | R2 | R1
Data | 1 | 0 | 0 |  | 1 | 1 | 0 |  | 1 |  | 
R1 | 1 |  | 0 |  | 1 |  | 0 |  | 1 |  | R1=1
R2 | 1 | 0 |  |  | 1 | 1 |  |  | 1 | R2=0 | 
R4 |  |  |  |  | 1 | 1 | 0 | R4=0 |  |  | 
R8 | 1 | 0 | 0 | R8=1 |  |  |  |  |  |  | 
Data to be transmitted | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 1
Data to be transmitted : 10011100101

## Slide 38: 5. Hamming Code
Data Received: 11011100101 calculate parity including R bits
R8 R4 R2 R1 = 1010 => 10th bit is error
 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
 | D6 | D5 | D4 | R8 | D3 | D2 | D1 | R4 | D0 | R2 | R1
Data | 1 | 1 | 0 |  | 1 | 1 | 0 |  | 1 |  | 
R1 =0 | 1 |  | 0 |  | 1 |  | 0 |  | 1 |  | R1=1
R2=1 | 1 | 1 |  |  | 1 | 1 |  |  | 1 | R2=0 | 
R3=0 |  |  |  |  | 1 | 1 | 0 | R4=0 |  |  | 
R4=1 | 1 | 1 | 0 | R8=1 |  |  |  |  |  |  | 
Data to be transmitted | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 1

## Slide 39: Index
Ethernet (IEEE 802.3)
Functions of Data Link Layer
  Error Control
  Flow Control
  Medium Access Control

## Slide 40: Flow Control
Automatic Repeat Request (ARQ) protocol
  Stop and Wait
  Go back N
  Selective Repeat

## Slide 41: Stop and Wait ARQ

## Slide 42: Stop and Wait ARQ

## Slide 43: Go back N ARQ

## Slide 44: Goback N
Lost frame

## Slide 45: Goback N
Lost ACK

## Slide 46: Selective Repeat

## Slide 47: Selective repeat

## Slide 48: Selective repeat

## Slide 49: Index
Ethernet (IEEE 802.3)
Functions of Data Link Layer
  Error Control
  Flow Control
  Medium Access Control

## Slide 51: Medium Access Control (MAC)
Aloha
Slotted Aloha
CSMA
CSMA/CD

## Slide 52: Pure Aloha

## Slide 54: Slotted Aloha

## Slide 56: CSMA

## Slide 57: Reservation

## Slide 58: Polling

## Slide 59
Figure 12.21 Frequency-division multiple access (FDMA)

## Slide 60
Figure 12.22 Time-division multiple access (TDMA)

## Slide 62: Physical LAyer

## Slide 63: Modulation Techniques
Digital Data digital Transmission
Digital Data Analog Transmission
Analog Data Analog Transmission
Analog Data Digital Transmission

## Slide 64: Digital Data Digital Transmission

## Slide 66: QAM
Quadrature Amplitude Modulation
Constellation diagram

## Slide 67: Analog Data to Analog Transmission
Amplitude Modulation
Frequency Modulation

## Slide 68: Analog Data to Digital Transmission

## Slide 69: Analog Data to Digital Transmission
Delta modulation