## Slide 1: Transport Layer Protocols
Dr. Geetha V
Asst Professor,
Dept of IT,
NITK, Surathkal

## Slide 2: Index
Introduction
TCP Header Format
3. TCP state diagram

## Slide 3: Message Transmission using Layers [1]

## Slide 4: Functions of Transport Layer
Guarantees message delivery
Delivers messages in the same order they are sent
Delivers at most one copy of each message
Supports arbitrarily large messages
Supports synchronization between the sender and receiver
Allows the receiver to apply flow control to the sender
Supports multiple application processes on each host

## Slide 5: Limitations of Network Layer
Drop messages : Due to link failure or buffer full
Reorder messages: Due to packets may travel in different path
Deliver Duplicate copies: Due to timeout
Limit messages to some finite size: Due to network limitation
Deliver messages after an arbitrarily long delay: due to delay in path or queue

## Slide 6: TCP Header Format

## Slide 7: TCP Header
Total data bytes:
65,535-20-20=65,515 bytes (TCP Header 20 and IP header 20)
Source and Destination Port:

## Slide 8: TCP Header
Sequence Number (x) and Acknowledgement Number (x+1) :- Indicates the next byte to be received.
    32 bit => its numbers are based on number of bytes
Example: explain

## Slide 9: TCP Header
Offset/TCP header length (no. of words) : number of 32 bit words in header
  5 words => 5 x 4 = 20 bytes (without Options)
Options:
  U: URG: Urgent Pointer: U=1 Urgent pointer is valid
  A: ACK: A=1 Acknowledgment is Valid
  P: PSH: P=1: Push data to application upon arrival
  R: RST: R=1 Reset the connection
  S: SYN S=1 and A=0: Establish Connection
  F: FIN F=1: Release a connection

## Slide 10: TCP Header
Window Size:
  Sliding window flow control
  How many bytes may be sent starting at the byte acknowledged
  Synchronization ( 3 way handshake between sender and receiver)
  Window size advertisement (example)
    Nagle’s Algorithm: Send one byte from sender and buffer other bytes till it receives ACK
    Issue - Low bandwidth utilization
    Silly Window syndrome : Sending large blocks from sender and receiver, buffer is full and ACK for every byte getting free.
    Issue – Every byte extra header overhead (TCP and IP)
    Clark’ s Solution: Receiver must wait and advertise only when sufficient buffer space is available
    Issue: Sender must wait and it may increase response time.

## Slide 11: TCP Header
Checksum
  To ensure reliability
  Checksum is calculated with set of 16 bit words
  Initial value for checksum is 0’s
  Calculate checksum including Pseudo header +TCP header and Payload
  Sender side: Algorithm: add all 16 bit words 1’s complement
  Checksum is 1’s complement of the sum
  Receiver side: calculate checksum: if the result is zero accept the segment.

## Slide 12: TCP Header
Source Port number = 80 0x50 | Destination Port number=80 0x50
Sequence number = 512 0x200 | 
Acknowledgement = 1024 0x400 | 
Offset=5 Res =0 flags: U A P R S F | Window Size = 1024 0x400
Checksum = 0x00 (Initialization) | Urgent Pointer=0x00
Source address= 198.35.65.5
Destination address: 199.27.46.9
Reserved: 0x00 Protocol: 0x06 (tcp) TCP length: 20 0x14
Pseudo header
TCP header

## Slide 13: TCP Header
Source Port = 0000 0000 0101 0000 | Destination Port = 0000 0000 0101 0000 | 
Sequence number = 0000 0000 0000 0000 0000 0010 0000 0000 |  | 
Acknowledgement = 0000 0000 0000 0000 0000 0100 0000 0000 |  | 
Offset=0101 flags: 0000 0001 0000 |  | Window Size =0000 0100 0000 0000
Checksum =0000 0000 0000 0000 |  | Urgent Pointer= 0000 0000 0000 0000
Source address= 11000110.00100011.01000001.00000101
Destination address: 11000111.00011011.00101110.00001001
Reserved: 0000 0000 Protocol: 0000 0110 TCP length: 0001 0100 pad: 0000 0000
Pseudo header in bits
TCP header in bits

## Slide 14: TCP Header Checksum
1100 0110 0010 0011
0100 0001 0000 0101
1100 0111 0001 1011
0010 1110 0000 1001
0000 0000 0000 0110
0001 0100 0000 0000
0000 0000 0101 0000
0000 0000 0101 0000
0000 0000 0000 0000
0000 0010 0000 0000
0000 0000 0000 0000
0000 0100 0000 0000
0101 0000 0001 0000
0000 0100 0000 0000
0000 0000 0000 0000
0000 0000 0000 0000
Sum= 0110 1011 0000 0100
Take 1s complement of sum
0110 1011 0000 0100
That is
1001 0100 1111 1011
So check sum is
1001 0100 1111 1011

## Slide 15: TCP Header
Source Port = 0000 0000 0101 0000 | Destination Port = 0000 0000 0101 0000 | 
Sequence number = 0000 0000 0000 0000 0000 0010 0000 0000 |  | 
Acknowledgement = 0000 0000 0000 0000 0000 0100 0000 0000 |  | 
Offset=0101 flags: 0000 0001 0000 |  | Window Size =0000 0100 0000 0000
Checksum =1001 0100 1111 1011 |  | Urgent Pointer= 0000 0000 0000 0000
Source address= 11000110.00100011.01000001.00000101
Destination address: 11000111.00011011.00101110.00001001
Reserved: 0000 0000 Protocol: 0000 0110 TCP length: 0010 1000 pad: 0000 0000
Pseudo header in bits
TCP header in bits

## Slide 16: TCP Header
Urgent Pointer:
eg: Upload of large data and TELNET working simultaneously
Portion of data requested by receiver as urgent

## Slide 17: Synchronization
Sender
Receiver
SYN
SYN_REVD
SYN +ACK
SYN_SENT
ESTABLISHED
ACK
ESTABLISHED
Data transfer state

## Slide 18
CLOSED
ESTABLISHED
SYN_SENT
SYN_RECD
LISTEN
Starting Point
Appl: passive open
Send: Nothing
Appl: active open
Send: SYN
Active Open
Appl: close
Or timeout
Recv:SYN;
Send: SYN,ACK
Recv: RST
Passive Open
recv: SYN
Send: SYN,ACK
Simultaneous Open
recv: ACK
Send: <nothing>
Recv:SYN,ACK
Send:ACK
Appl: send data
Send: SYN
Timeout
Send: RST
https://www.tangentsoft.net/wskfaq/articles/debugging-tcp.html
1
4
3
2
5
6
7

## Slide 19: Closing Connection 1

## Slide 20
1
2
3
4
5
6
7
8
9
MSL: Maximum Segment Lifetime is the time a TCP segment can exist in the internetwork system. (approx 2 min)

## Slide 22: Congestion Control in Transport Layer

## Slide 23: UDP (User Datagram Protocol)

## Slide 24: Reference
http://what-when-how.com/data-communications-and-networking/network-and-transport-layers-data-communications-and-networking/
Computer Network : Andrew S Tanenbaum